## Slide 1
Reminding for Project2
If not halting by error, you should filled up with 5 halt instruction in pipeline to
halt simulation.
In 2nd submission, your testcase is valid if
Student’s
testacse
Student’s
simulator
TA’s
simulator
*.rpt
*.rpt

## Slide 2: Computer Architecture
Project3 Tutorial

## Slide 3
Virtual Memory in Modern System
core
i-tlb
d-tlb
d-cache
i-cache
Disk
CPU
Memory
Page Table

## Slide 4
Project Goal
error handler
TLB
Page table
Memory
Disk
Cache
Execute one instruction as project 1
Compute TLB/PageTable/Cache hits/misses
In each cycle
Testcase Note
「write register 0 」and 「number overflow」errors are allowed
「memory address overflow」 and 「memory address misaligned」 are not allowed

## Slide 5
System Architecture
CPU
i-tlb
i-cache
i-mem
i-page
table
i-disk
(iimage.bin)
VA(PC)
1a.hit
1b.miss
2d.miss
3c.miss
2a.hit
2b.miss
2c.hit
3a.hit
3b.hit
d-tlb
d-page
table
4b.miss
5c.hit
d-cache
4a.hit
d-mem
5b.miss
6a.hit
5d.miss
6b.hit
d-disk
(dimage.bin)
6c.miss
load/store
Instruction
5a.hit
PageTable hit  update TLB  search cache
PageTable missSwapupdate PageTableupdate TLBupdate cache
Memory hit update PageTable update TLB  search cache
Memory missSwapupdate PageTable update TLB  update cache
Note
Cache & Memory adopt write-back/allocate policy
TLB & Cache & Memory adopt LRU replacement policy

## Slide 6
Input
The same as previous project’s format
  iimage.bin
  dimage.bin
Invalid testcase
  i-memory & d-memory address overflow
  i-memory & d-memory misaligned
  Simulation cycles over 500,000
Output
snapshot.rpt
  -register file content at each cycle
report.rpt
  -total number of TLB/PageTable/Cache hits/misses

## Slide 7
Execution Parameter
./CMP [P1] [P2] [P3]… [P10]
[P1]: The instruction memory (I memory) size, in number of bytes
[P2]: The data memory (D memory) size, in number of bytes
[P3]: The page size of instruction memory (I memory), in number of bytes
[P4]: The page size of data memory (D memory), in number of bytes
[P5]: The total size of instruction cache (I cache), in number of bytes
[P6]: The block size of I cache, in number of bytes
[P7]: The set associativity of I cache
[P8]: The total size of data cache (D cache), in number of bytes
[P9]: The block size of D cache, in number of bytes
[P10]:The set associativity of D cache
./CMP
You should support default configuration
(P1,P2,…,P10) = (64,32,8,16,16,4,4,16,4,1)

## Slide 8
Evaluation Note
For each testcase, TA will use default configuration to evaluate
In 1st & 2nd, TA will choose two other configurations,
  -you will get 10% discount if you fail one of them
  -you will get 19% discount if you fail both of them
 | default | config1 | config2 | Final score
tescase1 | pass | pass | pass | 1
testcase2 | pass | fail | pass | 0.9
testcase3 | pass | pass | fail | 0.9
testcase4 | pass | fail | fail | 0.81
Example: (assume each testcase is 1 point)